## Slide 1: Autonomous Vehicle Development
Center for Intelligent Machines and Robotics
University of Florida

## Slide 2: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 3: Navigation with Static Obstacles
DARPA Grand Challenge, 2004 & 2005.
Problem Statement
  given: a 225 km path defined by a series of waypoints
  navigate the entire path as quickly as possible

## Slide 5: Technical Challenges
off-line path planning
detection of static obstacles
environment data represen-tation and sensor integration
localization
interprocess communication and coordination of multiple threads on multiple computers
reconciliation of differences in estimated global pose, a priori data, and sensed information
fault tolerance

## Slide 6: Vehicle System
single primary behavior
  position vehicle in corridor
  locate any obstacles in corridor
  identify best terrain in corridor
  go fast
be ready to run on 27 Sep 05

## Slide 7: Sensor Systems
design of sensing system
  pose
    Starfire GPS
    Smiths Aerospace IMU
  obstacles
    bumper height ladar
  terrain
    two stationary ladar
    image processing
  implementation of sensor arbitration via traversability grid
ladar
monocular vision
ladar

## Slide 8
60 m  60 m grid with
grid resolution of 0.5 m  0.5 m

## Slide 10: 2005 DARPA GC Results
23 vehicles left the starting line
5 vehicles completed the 132 mile course
  Stanford Stanley
  CMU Sandstorm
  CMU Highlander
  Gray Team Kat 5
  Oshgosh Terra Max

## Slide 11
After 14 miles of travel, UF system had an 8 meter error in GPS position (vehicle thought the centerline of the corridor was off to the right).
Upon reaching this road junction, the vehicle moved to the right.

## Slide 12: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 13: Urban Area Nav. Problem Statement
given:
  Road Network Data File
  Mission Data File
do the following:
  visit the waypoints listed in the Mission Data File
  obey traffic laws

## Slide 14: Sample Road Network Data File (RNDF)
RNDF_name Sample_RNDF_Rev_1.5
num_segments 13
num_zones 1
format_version 1.0
creation_date 29-Mar-07
segment 1
num_lanes 2
segment_name Michigan_Ave
lane 1.1 /*no exits, passing lane*/
num_waypoints 4
lane_width 12
left_boundary double_yellow
right_boundary broken_white
1.1.1 38.875413 -77.205045
1.1.2 38.875471 -77.204189
1.1.3 38.875585 -77.202593
1.1.4 38.875673 -77.201373
end_lane
lane 1.2
num_waypoints 6
lane_width 12
left_boundary broken_white
exit 1.2.4 3.1.1
exit 1.2.6 4.1.1
1.2.1 38.875343 -77.205619
1.2.2 38.875438 -77.204198
1.2.3 38.875528 -77.202959
1.2.4 38.875602 -77.201871
1.2.5 38.875616 -77.201664
1.2.6 38.875676 -77.200830
end_lane
end_segment

## Slide 15: Sample Mission Data File (MDF)
MDF_name Sample_MDF_Rev_1.5
RNDF Sample_RNDF_Rev_1.5
format_version 1.0
creation_date 30-Jan-07
checkpoints
num_checkpoints 18
1
2
3
2
3
2
3
4
2
4
2
14 /*parking spot*/
5
10
17 /*parking spot*/
6
7
8
end_checkpoints

## Slide 16: 2007 Urban Challenge
Basic Navigation
  stay in lane
  passing
  U turn
Basic Traffic
  intersections
  minimum following distance
Advanced Navigation
  obstacle field
  parking lot
  dynamic replanning
  road following
  GPS outage
Advanced Traffic
  merging
  left turn in traffic
  defensive driving
  traffic jams
3 Nov 2007

## Slide 17: Basic Navigation

## Slide 18: Basic Navigation

## Slide 21: New Technical Challenges
pavement (road) detection and lane detection
detection and classification of dynamic objects
reconciliation of differences in estimated global pose, a priori data, and sensed information
determination of appropriate behavior mode
smooth transition of vehicle control between behavior modes

## Slide 22: Urban NaviGator
Hybrid Toyota Highlander
Sensors
  Smiths NFM integrated with Novatel and Garmin GPS and wheel encoders
  6 Sick ladars
  2 long range Sick ladars
  6 Bluefox cameras

## Slide 23: High Level of Complexity
6 primary behavior modes
  roadway navigation behavior
  open area navigation behavior
  parking lot behavior
  n-point turn behavior
  intersection behavior
  passing maneuver behavior
UF team developed and implemented the Adaptive Planning Framework
  decides upon the best current behavior mode

## Slide 24
FINDINGS
EVALUATE
BEHAVIORS
SELECT
BEHAVIOR

## Slide 26
Test Area A
tested moving obstacles

## Slide 27: Test Area A

## Slide 28: Finals
11 Teams Selected
CMU
VT
Stanford
Penn
UCF
MIT
Cornell
Oshkosh
Honeywell
Braun-
schweig
Karlsruhe

## Slide 29: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 30: Convoy Operations - Important Points
Human driven leader vehicle.
Automated follower vehicle.
Design Constraints
  No radio communication between any vehicle
  No GPS on any vehicle

## Slide 31: Controller

## Slide 32: Tether Approach

## Slide 33: Vision approach
  infrared emitters attached to back of leader vehicle
  panning camera mounted on follower
  measures distance and angle to leader (exact same data as obtained by tether)

## Slide 36: Vision Sensor

## Slide 37: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 38: Autonomous Range Clearance
Four steps
    vegetation removal

## Slide 39: Autonomous Range Clearance
Four steps
    vegetation removal
    surface object removal

## Slide 40: Autonomous Range Clearance
Four steps
    vegetation removal
    surface object removal
    mapping of subsurface objects

## Slide 41: Autonomous Range Clearance
Four steps
    vegetation removal
    surface object removal
    mapping of subsurface objects
    digging and removal of subsurface objects

## Slide 42: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 43: Vehicle / Manipulation Integration

## Slide 44: Objective
Command and control the contact interface between the payload and target.
Specifically control how the two touching bodies apply constraint wrenches to each other as well as how the bodies freely twist relative to each other.
Implemented using screw theory.
  wrench of constraint
  twist of freedom

## Slide 45: Objective
Simultaneously control contact forces and position.
Implemented using screw theory.
  wrench of constraint
  twist of freedom

## Slide 46: Terminology
twist
  an instantaneous motion
  can always be represented as a rotation about a line in space, coupled with a translation along that line
{0S1 ; 0S10L}
01
0h1

## Slide 47: Terminology
wrench
  a force / torque state
  can always be represented as a force along a line in space, coupled with a torque about that line
{Sf ; Sf_0L}
f
hf

## Slide 48: Terminology
When a body is in contact with the environment,
  twists of freedom are the still achievable motions
  01 {0S1 ; 0S10L+ 0h1 0S1} twist of freedom
  wrenches of constraint are the contact force and torque that will generate no motion of the body
  f {Sf ; Sf_0L + hf Sf} wrench of constraint
  wrenches of constraint are reciprocal to the twists of freedom
  0S1  (Sf_0L + h Sf) + Sf  (0S10L+ h 0S1) = 0

## Slide 49: Kinestatic Control Introductory Example
The compliance matrix is a key part of the Kinesthetic Control approach.

## Slide 50: Kinestatic Control Introductory Example
Compliance is introduced between the end of the robot (body 1) and the body that contacts the environment (body 2).
We can determine the compliance matrix-
  this relates the change of the contact wrench to the change in the relative pose between bodies 1 and 2
body 1
body 2
compliant
element

## Slide 51: Testbed for this Work

## Slide 52: Testbed for this Work

## Slide 53: Spring Elements

## Slide 54: Sensed Inputs K matrix evaluated at each instant
f1
f2
f3
x1
x2
y1
y2

## Slide 55: Control Schema
high-level assembly task supervisor
  develops overall assembly plan
  maintains an instantaneous model of available twists of motion and current wrenches of constraint
  based on current step of assembly operation, generates a desired motion twist and a desired contact wrench
mid-level explicit kinestatic controller
  via kinestatic control, actuator forces are determined which will achieve the desired motion twist and the desired contact wrench
low-level force controller
  conventional force control of individual actuators

## Slide 56: Task
payload
F
G
Tangency line
Target
payload
F
G
Tangency line
Target
payload
F
G
tangency line
target
Case 0
Case 1
Case 2
Case 3

## Slide 57
desired twist for case i
deflection wrenches for case i
set of wrenches that span space
decompose the sensed wrench

## Slide 58
desired twist for case i
deflection wrenches for case i
set of wrenches that span space
decompose the sensed wrench
payload
F
G
Tangency line
Target

## Slide 59
desired twist for case i
deflection wrenches for case i
set of wrenches that span space
decompose the sensed wrench
payload
F
G
Tangency line
Target

## Slide 60
desired twist for case i
deflection wrenches for case i
set of wrenches that span space
decompose the sensed wrench
payload
F
G
tangency line
target

## Slide 61: Summary
at each instant
  three leg lengths are known
  force in each leg is known
  calculate net wrench,
  determine twists of freedom and use K matrix to get deflection wrenches
  project net wrench on wrenches of constraint and deflection wrenches
  consider each of 5 contact cases and determine case based on heuristic rules
  select magnitudes for constraint wrench and deflection wrench to correct any error in contact wrench and to cause the desired twist
  decompose the net total desired wrench into individual leg forces and command the legs

## Slide 62: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 63: Adjustable Stiffness Suspension Mechanism
Objective
  Develop a suspension system that isolates a car body from road disturbances by mechanically adjusting it’s effective stiffness.
Approach
  Application of a recently designed variable stiffness mechanism.

## Slide 64: Variable Stiffness Mechanism
Schematic: Variable Stiffness Mechanism

## Slide 65: Effective Stiffness

## Slide 66: Plot of Effective Stiffness
Aspect Ratio

## Slide 67: Determination of Free Length
Overall Free Length

## Slide 68: Plot of Overall Free Length

## Slide 69: Application to Suspension System
Schematics: Variable Stiffness Suspension Mechanism

## Slide 70
Parameters
Effective Stiffness
Overall Free Length

## Slide 71: Plot of Effective Stiffness

## Slide 72: Passive vs. Active System

## Slide 73: Controller Design
H-infinity Design Block Interconnection Diagram
ride comfort
road holding
suspension
deflection

## Slide 74: Performance Weights
  Ride Comfort
  Suspension Deflection
  Road Holding
(ISO 2631, 1997)

## Slide 75: Discrete Event Road bump at speed of 40 mph
(m)

## Slide 76: Discrete Event – Time Domain Results
Road bump at speed of 40 mph
m/sec2
m
m

## Slide 77: Discrete Event – Time Domain Results

## Slide 78: New Design
Current Design

## Slide 80: Conclusion
The performance of vehicle suspension can be improved by varying the stiffness of the suspension element.
Passive Variable Stiffness Suspension Mechanism improves the ride comfort but degrades the suspension deflection.
Active Variable Stiffness Suspension Mechanism provided the best trade off between Ride comfort, Suspension deflection and Road holding.
Future work will be to optimize the design for compactness.

## Slide 81: Topics
History
  Autonomous navigation with static obstacles.
  Autonomous navigation in an urban environment.
  Application: Autonomous convoy operations.
  Application: Automated range clearance.
Direction of Research
  Manipulation.
  Vehicle performance.
  New research thrusts.

## Slide 82: Research Direction
Image-based Estimation and Control
  Keeping objects in the field of view (FOV).
  Alternative guidance navigation & control for unmanned vehicle.
  Improved pose (position and orientation) estimation.
  Geo-location and geo-referencing using videos.
Intelligent Autonomy
  Human and machine interaction with shared intelligence.
  Intelligent control methods – e.g., actor critic, reinforcement learning, learn from experience.
Infrastructure Improvement to Aid Autonomy
  Peer to peer vehicle communication.
  “Smart” intersections.
Sensing
  tall grass problem

## Slide 83: Thank You